## Slide 1: New OSCON Series – line up
SVP (SMD)
105℃2,000h
2.5～20V
4x5.5～10x12.7
SVPF(SMD)/SEPF(THD)
105℃5,000h
16～50V
5x6～10x12.7
SXV(SMD)/SXE(THD)
125℃1,000h
(105℃5,000h)
63, 80, 100V
8x7～10x12.7
-High Voltage
Standard
Product
SVPA (SMD)
105℃2,000h
2.5～20V
5x6～10x8
SVPC (SMD)
105℃2,000h
2.5～16V
5x6～10x12.7
SVPE (SMD)
105℃2,000h
2.5～16V
5x6～10x12.7
SVPG(SMD)/SEPG(THD)
105℃5,000h
16V ～25V
5x4.4 ～ 6.3x10
SVPK(SMD)/SEK(THD)
125℃1,000h
(105℃2000h)
16～50V
5x6～10x12.7
-High Temp(125℃)
-High Voltage
-High Temp(125℃)
-Large Cap
-High Ripple Current
-Low ESR
125℃ Products
-Low ESR
-Large Cap.
-Low ESR
105℃ Products
SVF(SMD)/SEF(THD)
125℃1,000h
(105℃5,000h)
16～50V
5x6～10x12.7
New
New
New
Notes: SEPG series is suitable as a smoothing capacitor, enabling miniaturizing switching power supplies, because it allows large ripple current, 5.8 Amps.
Its ESR, 8mohm max, has stable characteristics at a temperature from -55°C to 105°C, suitable for applications used at low temperatures (under 0°C). It also has excellent moisture resistance, very good for outdoor applications.
Feature: High Ripple & Low ESR  can miniaturizing your board (reduce use number) can support high current line
Long Life & excellent moisture resistance  Maintenance free or less for industrial use (outdoor or long life needed)
Stable characteristic not dependent on temperature and voltage  can use up to 100% spec written in datasheet (no derating)
Markets&Applications:
Base Station  Change from macro cell to small cell
E-Meter  Back up for power supply
Industrial Display  High grade visual spec (4k, 8k)
Server / Data center  Increase volume of traffic data by high desnity board
Security Camera, PV Inverter  To guarantee on severe environment
SXV/SXE: These series can offer both of large capacitance and low ESR at high voltage zone (up to 100V). It is very tough low ESR capacitor (High ripple current, high temperature, High voltage, large capacitance and ideal frequency/temperature characteristics) Usually each category of Capacitor has some week points but this OSCON is very strong for all check points.
Actual use condition Ripple Within the rated ripple current(Case1) Within the rated allowable ripple current(Case2)
Temp. Tx≦125℃ Tx≦105℃
Series To[℃] Lo[hrs] Lx@105℃[hrs] Lx@85℃[hrs] To[℃] Lo[hrs] Lx@105℃[hrs] Lx@85℃[hrs]
SVX/SXE 125 1,000 10,000 100,000 105 5,000 5,000 50,000
SVPK 125 1,000 10,000 100,000 105 2,000 2,000 20,000
SVF/SEF 125 1,000 10,000 100,000 105 5,000 5,000 50,000
SVPF/SEPF ― ― ― ― 105 5,000 5,000 50,000

## Slide 2: Lytics SMD Roadmap
Temperature
Lower ESR
VS
HA
HB
HC
HD
FC
FK
FP
TG
TK
TC
TQ
105ºC 2000h 60mΩ
105ºC 1000h 150mΩ
105ºC 2000h 80mΩ
105ºC 2000h
105ºC 3000h
105ºC 5000h
105ºC 1000h
85ºC 2000h
125ºC 2000h 300mΩ
125ºC 3000h 200mΩ
FTG
T*
Downsizing
125ºC 4000h
ZA
ZC
105ºC 10000h
ZE
TP
Long life
Downsizing
TCU
FT
F-Family
(Low ESR)
Hybrid Capacitor
High ripple current
Large Cap.
T-Family
(High-temperature)
FKS
Large Cap.
Higher ripple
-50% ESR / low temp
FTU
Miniaturized
Longer Life / Miniaturized
CONFIDENTIAL
ZK
145ºC 2000h
NPI
LE
1 size smaller comp. TK
Notes: ZK has higher Ripple and higher capacitance compared to ZC
From 125°C and below ZE behaves like ZC
ZE scheduled for June 2017 / Q2 2017
ZE  8000h at 125°C

## Slide 3: Lytics SMD Roadmap
Longer Life / Miniaturization
LOW ESR
VS
HA
HD
TG
FC
FK
FP
TK
FTU
Confidential
Temperature
HB
HC
FKS
TC
TP
TQ
TCU
FT
Low ESR
High Temp.
Commodity
Notes: TP: adding bigger case sizes and higher voltages
FK continuous to dominate the market, with FKS we offer cost reduction due to lower case sizes

## Slide 4: EDLC Line-up / Radial lead Type
Radial lead Type
Series HW  18
22F-70F
-25℃～+70℃
Series HZ  8/10
3.3-10F
-25℃～+70℃
70℃ 2.5V 1000h
70℃ 2.3V 1000h
High Capacitance / Small package
Standard
High Voltage / Low ESR / Long Life
Back up for mA-A
Main Applications : Back up for E-meter
For Industrial
For Automotive
Series HL (Large Cell)  18x50/70
50F/100F
15mΩ/10m Ω
-40℃ to +65℃
65℃ 2.7V 2000h
New
High Voltage / Long Life
Series HL (Small Cell)
 8x20 – 10x30
2,5F-7,5F
30mΩ-70mΩ
-40℃ to +85℃
70℃ 2.7V 2000h
85℃ 2.5V 1000h
New
Miniaturized
Notes: Wound type- HZ and HW were older series – distinction is size and ESR. HL introduced in 2016 after 8 years of development work on electrolyte. Purple sleeve signifies new electrolyte
Radial lead type. This is used to usage of large current discharge. Current model are only HZ and HW. Today I want to introduce series HL.
Used for applications that need large current.
Very low internal resistance
Application: memory back up, motor driving
i.e. motor can work over 3 minutes with charging time of a few seconds
over 100k charge/discharge is possible
Suitable for toys and LEDs
Applications:
Solar battery circuit (e.g. Road guidance flasher, LED light
Toys (motor drive)
Server/Storage
LED lights – charged during daylight, discharged at night